Comparative thermodynamics analyses of gasoline and hydrogen fuelled Internal Combustion Engines

M. Faizala, R. Saidurb

aFaculty of Engineering, Universiti Industri Selangor, 45600 Selangor, Malaysia

bDepartment of Mechanical Engineering, University of Malaya, 50603 Kuala Lumpur, Malaysia

Abstract

Comparative thermodynamics models for naturally aspirated gasoline and hydrogen fuelled spark ignition internal combustion engines were developed according to the first and second law of thermodynamics. Analysis of mean effective pressure, power, torque, exergy due to heat transfer, exergy due to work, and irreversibility was made. Thermodynamics model was developed according to Ideal Otto cycle. Assumptions were made according to air standard assumptions.  First law efficiency, mean effective pressure, power, and torque of hydrogen fuelled internal combustion engine are higher than gasoline fuelled internal combustion engine due to higher compression ratio associated with hydrogen fuelled internal combustion engine, 14.5:1 compared to 8:1 of gasoline fueled internal combustion engine. Hydrogen fueled internal combustion engine can have higher compression ratio because of higher auto-ignition temperature, 858°C associated with hydrogen fuel compared to 300-450°C for gasoline fuel. All results were shown and graphed in this paper. A second law analysis shown that hydrogen fuelled internal combustion engine had higher second law efficiency of 69.40% compared to 60.49% for a gasoline fuelled internal combustion engine due to significantly lower irreversibilities and lower specific fuel consumption for a hydrogen fuelled internal combustion engine. The greater exergy due to heat transfer of hydrogen fuelled internal combustion engine occurs due to a greater amount of heat generated from hydrogen combustion. However, the high available thermal energy or thermal exergy of hydrogen fuelled internal combustion engine needs higher cooling load which decreases the power of hydrogen fuelled internal combustion engine. The combustion irreversibilities were constructed and discussed in this paper according to information found in literature reviews.

Key Words: Exergy; Thermodynamics; 1st and 2nd law analysis; hydrogen fuel; internal                   combustion engine

Topic: Hydrogen fueled transportation

aCorrespondence to: M. Faizal, Faculty of Engineering, Universiti Industri Selangor, Bestari Jaya Campus, Jalan Timur tambahan, Bestari Jaya, 45600 Selangor, Malaysia.

HP: 017-6620943	E-mail: mohdfaizalfauzan@yahoo.com

- Introduction

Demand and usage of energy is increasing throughout the world. Pollution increased. Current energy sources are depleting.  In recent years, the economy of Malaysia grew rapidly. The private vehicle populations grew rather in an escalating manner. This phenomenal rise of vehicles number has increased energy consumption, especially fossil fuels. Consequently air pollution has increased to a remarkable extent. In 2002, the transportation sector of Malaysia used about 40% of the total energy consumed (Saidur et al., 2007). Valero et al. (2010) indicate that there might not be enough available resources to satisfy the predicted future mineral demand. The changing of fuel from gasoline to hydrogen demands a thermodynamic analysis to determine and predict changes in performance and efficiency. Exergy is an effective method using the conversion of mass and conversion of energy principles together with the second law of thermodynamics for the design and analysis of energy system (Dincer et al., 2004). Thermodynamics model will be developed according to Ideal Otto cycle (Cengel et al., 2007).  Analysis of mean effective pressure, power, torque, exergy due to heat transfer, exergy due to work, and irreversibilities will be determined, displayed, commented and reasoning provided. First and second law efficiencies for both gasoline and hydrogen fuelled will be derived from this analysis.

Some study had been made applying the second law of thermodynamics to internal combustion engines to diagnose losses and suggest solutions for improving engine performance and efficiency. A lot of work has been done also for alternative fueled engines. Bayraktar et al. (2005) has developed and validated an engine simulator to compare performance and emission characteristics of an engine working on LPG and gasoline. Mustafi et al. (2006), in their work compared power-gas with gasoline and natural gas (NG). Rakopoulos et al. (2006) shown that exergy of methane and methanol is lower than dodecane but the pollutant emissions decreased. Caton, (2000) state that the destruction of the fuel’s available energy due to the combustion process decreases for operation at higher temperatures. The highest availability was found to exist for the unreacted fuel. This represents a maximum potential to perform work. When this chemical energy is transformed into thermal energy, some portion (which depends on the final temperature) of the original availability is destroyed.

Hydrogen, being highly reactive, offers wide range of advantages in performance. One of the principal advantages that hydrogen has a fuel is the wide flammability limits (see Table 1). These wide limits allow that the combustion occurs with different equivalence ratios, in particular with slight mixtures, which makes relatively easy to operate an engine with hydrogen (Soberanis et al., 2009).

Table 1: The gasoline and other fuel properties (Pourkhesalian et al, 2010)

| Fuel type | RON | Formula | Molecular weight | Density | Heat of vaporization | Lower heating value | Stoichiometric air /fuel ratio |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | (kg/m3) | (kJ/kg) | (Mj/kg) |  |
| Gasoline | 95.8 | C8H16 | 106 | 750 | 305 | 44.0 | 14.60 |
| Methane | 120 | CH4 | 16 | 720 | - | 50.0 | 17.23 |
| Propane | 112 | C3H8 | 44 | 545 | 426 | 46.4 | 15.67 |
| Hydrogen | 106 | H2 | 2 | 90 | - | 120.0 | 34.30 |

Another benefit is the high energy density of the fuel, around 120 MJ/kg, superior value to that of gasoline (Sorensen, 2005). The minimum ignition energy and the wide range of flammability of hydrogen allow the presence of combustion at lower equivalence ratios than those with gasoline, and it can obtain a higher power at specific equivalence ratios. The higher power output of the engine, running with hydrogen, was about 80% of the power reached with gasoline. From the experiment conducted by Ganesh et al., (2008), volumetric efficiency was plotted versus power output and thermal efficiency versus equivalence ratio. In the first case, a higher volumetric efficiency, compared with that of gasoline, with a power output between 2 and 7 kW, was observed. In the case of thermal efficiency, it was reached a maximum of about 27%, at different speeds, over that with gasoline which is about 25% (Ganesh et al., 2008). When the compression ignition engine is fueled with hydrogen, in order to fulfill a homogeneous mixture, it will obtain a better combustion (Martı´nez et al., 2008). Masood et al. (2007), made experimental and computational work on a hydrogen diesel dual fuel engine, with hydrogen presence from 10 to 80% Vol. It was noticed that with the increase of hydrogen load the pressure increases at high compression ratios due to the high flammability and rate of combustion of hydrogen. Moreover, hydrogen has a major flame velocity at stoichiometric conditions, which makes the engine getting closer to the thermodynamically ideal engine. Hydrogen injection during compression stroke prevents knocking, increases thermal efficiency and maximizes the power output (Mohammadi, 2007). Knock, or spark knock (Topinka, 2004), is defined as autoignition of the hydrogen–air end-gas ahead of the flame front that has originated from the spark. The high autoignition temperature, finite ignition delay and the high flame velocity of hydrogen  means that knock, as defined, is less likely for hydrogen relative to gasoline, and hence the higher research octane number (RON) for hydrogen (RON>120) (Tang, 2002) in comparison to gasoline (RON=91−99) (Heywood, 1988).

Table 2: Ignition temperature and compression ratio used for various fuels

|  |  | Ignition Temperature | Compression ratio |  |
| --- | --- | --- | --- | --- |
| Fuel | Formula | (°C) | CR | Reference |
| Octane | C8H18 | 300 - 450 | 8.0 | Cengel (2007) |
| Hydrogen | H2 | 858 | 14.5 | Verhelst (2009) |
| Methane | CH4 | 813 | 15.0 | Gupta (2006) |
| Propane | C3H8 | 457 | 10.0 | Ozcan et al. (2008) |
| Methanol | CH4O | 574 | 11.0 | Li et al. (2010) |
| Ethanol | C2H6O | 537 | 10.0 | Park et al. (2010) |

In this paper, comparative thermodynamics analyses of gasoline and hydrogen fuelled internal combustion engines (ICE) are carried out and results are graphed and commented upon.

- Thermodynamic analysis

Thermodynamic analyses for both gasoline and hydrogen fuelled engine are going to be made based on air-standard Ideal Otto cycle (Pulkrabek, 2004) at 3000 RPM. Both engines will be four-cylinder, 2-liter, spark ignition, square engine. Combustion efficiency is assumed as 100%. It can be assumed that the initial conditions in the cylinder before compression stroke are 100 kPa and 30°C.

Process 1-2 – isentropic compression stroke:

(1)

(2)

(3)

Process 2-3 – constant-volume heat input (combustion):

(4)

(5)

(6)

(7)

Process 3-4 – Isentropic power stroke:

(8)

(9)

(10)

2.1 Mean Effective Pressure

Pressure in the cylinder of an engine is continuously changing during the cycle. An average or mean effective pressure (mep) for both gasoline and hydrogen fuelled engine is defined by (Pulkrabek, 2004).

(11)

2.2 Horsepower

Power is defined as the rate of work of the engine. If n = number of revolutions per cycle and N = engine speed, then (Pulkrabek, 2004)

(12)

Power is commonly measured in horsepower (hp)

(13)

2.3 Torque

Torque is a good indicator of an engine’s ability to do work. It is defined as force acting at a moment distance and has units of N-m. Torque τ is related to power by (Pulkrabek, 2004)

(14)

2.4 Exergy by heat transfer

Exergy by heat transfer is the work potential of the energy transferred from a heat source in a system taken from its initial temperature to temperature of the environment or dead state. Heat is a form of disorganized energy, and thus only a portion of it can be converted to work, which is a form of organized energy (the second law). Work can always be produced from heat at a temperature above the environment temperature by transferring it to a heat engine that rejects the waste heat to the environment. Therefore, heat transfer is always accompanied by exergy transfer. Heat transfer Q at a location at thermodynamic temperature T is always accompanied by exergy transfer Xheat in the amount of (Cengal et al., 2007)

Xheat =  	(15)

2.5 Exergy transfer by work

Work exergy is defined as the availability of the system to do actual work on the changing control volume against its surroundings. With respect to a piston-cylinder device, boundary work is the work required to move the piston against the boundary conditions and change the cylinder volume. The compression and expansion processes are assumed to be polytropic and as a function of cylinder volume (Cengal et al., 2007). Finally the exergy due to work can be given by:

Xwork = (16)

Where

Wsurr = P0 (V2 – V1)	(17)

2.6 Irreversibility

Any difference between the reversible work Wrev and the useful work Wu is due to the irreversibilities present during the process, and this difference is called irreversibility I. It is expressed as

I = Wrev,out – Wu,out 	(18)

The amount of the availability that is destroyed increases for lower final temperatures. During the combustion process, the availability destroyed by combustion is about 18.9%, and the availability destroyed by the heat transfer is about 12.0% (Hongqing et al., 2006). Soma et al. (2008) has recognized that, in almost all situations, the major source of irreversibilities is the internal thermal energy exchange associated with high temperature gradients caused by heat release in combustion reactions. The primary way of keeping the exergy destruction in a combustion process within a reasonable limit is to reduce the irreversibility in heat conduction through proper control of physical processes and chemical reactions resulting in a high value of flame temperature but lower values of temperature gradients within the system.

2.7 First and 2nd Law Efficiency

First Law efficiency is a measure of the performance of a heat engine according to the fraction of the heat input that is converted to net work output. The 1st Law efficiency of an engine can be expressed as (Cengal et al., 2007)

(19)

Or

Thermal efficiency of the Otto cycle at WOT can be determine by (Pulkrabek, 2004)

(20)

Second-law efficiency ηII is defined as the ratio of the actual thermal efficiency to the maximum possible (reversible) thermal efficiency under the same condition (Cengal & Boles, 2007). From irreversibility equation (3.19), the second-law efficiency can be expressed as the ratio of the useful work output and the maximum possible (reversible) work output:

(21)

Based on the above models, the first and second law efficiency can be calculated and graphed for both hydrogen and gasoline fuelled engines.

- Results and discussion

Table 3: Results obtained from calculation

|  | Net work output | 1st law efficiency | Mean effective pressure | Power output | Torque | Heat Exergy | Mechanical Exergy | Irreversibility | 2nd Law efficiency |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Wnet | ηth | mep |  | τ | Xheat | Xwork | I | ηII |
| Fuel | (kJ) | (%) | (kPa) | (hp) | (N-m) | (kJ) | (kJ) | (kJ) | (%) |
| Gasoline | 1.02 | 56.40 | 2040 | 136.76 | 325 | 1.69 | 1.07 | 0.67 | 60.49 |
| Hydrogen | 1.37 | 65.64 | 2740 | 183.70 | 436 | 1.97 | 1.37 | 0.60 | 69.40 |

3.1 Mean Effective Pressure

Figure 1: Comparison of mean effective pressure for gasoline and hydrogen fuelled engine

Figure 1 shown that mep for hydrogen fuelled engine is higher, 2740 kPa compared to gasoline, 2040 kPa. This result was due to higher work output associated with hydrogen fuelled engine. The higher work

output of hydrogen fuelled engine was caused by higher heat energy input from combustion because of higher heating value of hydrogen fuel, 120 MJ/kg compared to gasoline fuel, 44 MJ/kg (Pourkhesalian et al, 2009).

3.2 Horsepower

Figure 2: Comparison of horsepower for gasoline and hydrogen fuelled engine

Figure 2 illustrate that hydrogen has higher power output, 183.7 hp compared to gasoline, 136.76 hp. The results are relatively consistent with report from Sorensen, (2005) which also indicated that hydrogen can have higher power output than gasoline.

3.3 Torque

Figure 3: Comparison of torque for gasoline and hydrogen fuelled engine

Higher horsepower also means that the torque will be higher. Figure 3 shown that torque of hydrogen fuelled engine is higher, 436 N-m compared to 325 N-m associated with gasoline fuelled engine. Higher compression ratio (Verhelst, 2009) and higher pressure due to combustion of hydrogen fuelled engine are the major factors for the higher torque of hydrogen engine.

3.4 Exergy by heat transfer

Figure 4: Comparison of heat exergy for gasoline and hydrogen fuelled engine

Figure 4 shown that greater heat exergy for hydrogen engine compared to gasoline engine was due to higher combustion temperature associated with the hydrogen fuelled engine (Cengel, 2007). However, the high available thermal energy or thermal exergy of hydrogen fuelled internal combustion engine needs higher cooling load which decreases the power of hydrogen fuelled internal combustion engine (Shudo et al., 2002). The results obtained were consistent with studies by Nieminen et al. (2010) which illustrate the variation of exergy due to heat transfer as a function of crank angle.

3.5 Exergy transfer by work

Figure 5: Comparison of mechanical exergy for gasoline and hydrogen fuelled engine

Figure 5 shown that hydrogen have higher exergy due to work than gasoline fuelled engine due to higher temperature and pressure from combustion of hydrogen fuel (Cengel, 2007). However, Nieminen et al. (2010) in his studies stated that hydrogen has lower work exergy due to higher compression stroke associated with hydrogen fuelled engine. The transfer of exergy via compression work is the reason for the negative value of exergy.

3.6 Irreversibility

Figure 6: Comparison of irreversibility for gasoline and hydrogen fuelled engine

An irreversibility analysis is done for both gasoline and hydrogen combustion reactions using the approach from eq. 18. It was found that the combustion of hydrogen is less irreversible than the combustion of gasoline. The results are consistent with results reported by Nieminen et al. (2010).

3.7 1st and 2nd law efficiency

Figure 7: Comparison of 1st and 2nd law efficiency for gasoline and hydrogen fuelled engine

Figure 8 shown that both 1st law and second law efficiency for hydrogen engine is higher than gasoline engine 65.64, 69.4 % and 56.4, 60.5 % respectively. Nieminen et al. (2010) was also found that the hydrogen fuelled engine had a greater proportion of its chemical exergy converted into work, indicating a second law efficiency of 41.37% as opposed to 35.74% for a gasoline fuelled engine. The higher first law efficiency of hydrogen engine was due to higher compression ratio (Verhelst, 2009) and the higher second law efficiency associated with hydrogen engine is due to significantly lower irreversibilities of hydrogen engine (Cengel et al. 2007).

- Conclusions

This comparative thermodynamics analysis between gasoline and hydrogen fuelled internal combustion engines has indicated that a hydrogen fuelled engine is more efficient than a gasoline fuelled engine from the first law perspective, 65.64% to 56.4% and the second law efficiency, 69.4% to 60.5% respectively. The reasons include higher compression ratio and lower irreversibility associated with hydrogen engine. Finally, the analysis conducted in this study shows that a hydrogen fuelled engine indicates higher mean effective pressure, torque, power output, heat exergy and work exergy compared to gasoline engine because of higher temperature and pressure from hydrogen combustion.

References

M. Pourkhesalian, A. H. Shamekhi, F. Salimi.  Alternative fuel and gasoline in an SI engine: A comparative study of performance and emissions characteristics. Fuel 89 (2010) 1056-1063

Midilli, I. Dincer. Hydrogen as a renewable and sustainable solution in reducing global fossil fuel consumption, International Journal of Hydrogen Energy 33(2008) 4209 – 4222

Mohammadi, M. Shioji, Y. Nakai, W. Ishikura, E. Tabo. Performance and combustion characteristics of a direct injection SI hydrogen engine, International Journal of Hydrogen Energy 32 (2007) 296 – 304

C. D. Rakopoulus, E. G. Giakoumis. Second law analyses applied to internal combustion engine operations, Progress in energy and combustion science 32 (2006) 2-47

C. Park, Y. Choi, C. Kim, O. Seungmook, G. Lim, Y. Moriyoshi.  Performance and exhaust emission characteristics of a spark ignition engine using ethanol and ethanol-reformed gas, Fuel 89 (2010) 2118–2125

F. Hongqing, L. Huijie. Second-law analyses applied to a spark ignition engine under surrogate fuels for gasoline, Energy 3 (2010) 1010-1016

H. Bayraktar, O. Durgun. Investigating the effects of LPG on spark ignition engine combustion and performance, Energy Conversion and Management 46 (2005) 2317-2333

H. N. Gupta. Fundamentals of internal combustion engines, Prentice-Hall of India 2006

H. R. Ganesh, V. Subramanian, V. Balasubramanian, J. M. Mallikarjuna, A.  Ramesh, R. P. Sharma. Hydrogen fueled spark ignition engine with electronically controlled manifold injection: an experimental study. Journal of Renewable Energy 33 (2008) 1324–1333.

H. Ozcan, J. A. Yamin. Performance and emission characteristics of LPG powered four stroke SI engine under variable stroke length and compression ratio. Energy Conversion and Management 49 (2008) 1193–1201.

J. A. Caton. On the destruction of availability (exergy) due to combustion processes - with specific application to internal-combustion engines, Energy 25 (2000) 1097–1117

J. Nieminen, I. Dincer. Comparative exergy analyses of gasoline and hydrogen fuelled ICEs. International Journal of Hydrogen energy 35 (2010) 5124-5132

J. B. Heywood, Internal combustion engine fundamentals, McGraw-Hill Education, 1988.

M. A. E.  Soberanis, A. M. Fernandez. A review on the technical adaptations for internal combustion engines to operate with gas/hydrogen mixture, International Journal of Hydrogen Energy 70 (2009) 1010-1016

Mustafi, Y. C. Miraglia, R. R. Raine, P. K. Bansal, S. T. Elder. Spark-ignition engine performance with ‘Power-gas’ fuel (mixture of CO/H2): a comparison with gasoline and natural gas. Fuel 85 (2006) 1605–1612

R. Saidur, M. A. Sattar, H. H. Masjuki, S. Ahmed, U. Hashim. An estimation of the energy exergy efficiencies for the energy resources consumption in the transportation sector in Malaysia, Energy Policy 35 (2007) 4018–4026

S. Szwajaa, K. R. Bhandarya, J. D. Nabera. Comparisons of hydrogen and gasoline combustion knock in a spark ignition engine. International Journal of Hydrogen Energy 32 (2007) 5076 – 5087.

S. Verhelst, P. Maesschalck, N. Rombaut, R. Sierens. Increasing the power output of hydrogen internal combustion engines by means of supercharging and exhaust gas recirculation, International Journal of Hydrogen Energy 34 (2009) 4406–4412

Shudo. Improving thermal efficiency by reducing cooling losses in hydrogen combustion engines, International Journal of Hydrogen Energy 32 (2007) 4285–4293.

S. Yousufuddin, M. Masood. Effect of ignition timing and compression ratio on the performance of a hydrogen–ethanol fuelled engine. International Journal of Hydrogen Energy 34 (2009) 6945-6950.

W. Pulkrabek, Engineering fundamentals of the internal combustion engine, Pearson Prentice-Hall. 2004.

Y. A. Cengel, M. A. Boles. Thermodynamics: An engineering approach, McGraw-Hill Education. 2007.

Y. Azoumah, J. Blin, T. Daho. Exergy efficiency applied for the performance optimization of a direct injection compression ignition (CI) engine using biofuels. Renewable Energy 34 (2009) 1494–1500

Nomenclature

0	Dead state

BDC	Bottom dead center

CNG	Compressed natural gas

CR	Compression ratio

Cv	Specific heat (Cv = 0.718 kJ/kg ·K)

Hp	Horsepower

I	Irreversibility (J)

K	Ratio of specific heats (k=1.4)

LPG	Liquefied petroleum gas

m	mass (kg)

Max	Maximum

Mep	Mean effective pressure (Pa)

mf	Mass of fuel	(kg)

mm	Mass of mixture (kg)

N	Engine speed (m/s)

n	Revolutions per cycle

P	Pressure (Pa)

Q	Heat energy (J)

QHV	Heating value	(J)

Qin	Heat energy input (J)

R	Gas Constant (R=0.287 kJ/kg·K)

rc	Compression ratio

Rev	Revolution

RON	Research octane number

RPM 	Revolution per minute

surr	Surrounding

T	Temperature (K)

TDC 	Top dead center

Th	Thermal

u	Useful

V	Volume (m3)

Vd	Displacement volume (m3)

W	Work (J)

X	Exergy	 (J)

ηc	Combustion efficiency

τ	Torque (N – m)