Manuscript of paper from this project for journal FUEL

Table 1: The gasoline and other fuel properties [10]

| Fuel type | RON | Formula | Molecular weight | Density | Heat of vaporization at 298 K | Lower heating value | Stoichiometric air /fuel ratio |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | (kg/m3) | (kJ/kg) | (MJ/kg) |  |
| Gasoline | 95.8 | C7.56H15.5 | 106.22 | 750 | 305 | 44.0 | 14.60 |
| Methane | 120 | CH4 | 16 | 720 | - | 50.0 | 17.23 |
| Propane | 112 | C3H8 | 44 | 545 | 426 | 46.4 | 15.67 |
| Hydrogen | 106 | H2 | 2 | 90 | - | 120.0 | 34.30 |

Table 2: Ignition temperature and compression ratio used for various fuels

|  |  | Ignition Temperature | Compression ratio |  |
| --- | --- | --- | --- | --- |
| Fuel | Formula | (°C) | rc | Reference |
| Octane/gasoline | C8H18 | 300 - 450 | 8.0 | Cengel [4] |
| Hydrogen | H2 | 858 | 14.5 | Verhelst and Sheppard[14] |
| Methane | CH4 | 813 | 15.0 | Gupta[15] |
| Propane | C3H8 | 457 | 10.0 | Ozcan and Yamin [16] |
| Methanol | CH4O | 574 | 11.0 | Li et al. [17] |
| Ethanol | C2H6O | 537 | 10.0 | Park et al. [18] |